## Slide 1: Water Quality Management Plan (WQMP) March 6, 2025 Benjie Cho, P.E., QSD, TOR

## Slide 2: Why do we choose to be engineers?

## Slide 3: overview
NPDES Background
Preliminary WQMPs (P-WQMP)
Final WQMPs (F-WQMP)
MS4 Permit Negotiations

## Slide 4: NPDES Background

## Slide 5: NPDES Background
Cuyahoga River, OH November 4, 1952

## Slide 6: NPDES Background
The Clean Water Act (1972)
Enacted the Federal NPDES Program
www.epa.gov
http://www.dep.state.pa.us/earthdaycentral/01/b4wastwat.htm
Point sources

## Slide 7: NPDES Background
California Porter Cologne Act (1969)
Requirements for Waste Dischargers
MS4 Permits are for both
Federal State

## Slide 8: NPDES Background
The Clean Water Act Amendments (1987)
  Expanded to include storm water
130.11.63.183/water.html
Non-Point sources
Surface flow, streets, and MS4’s.

## Slide 9: NPDES Background

## Slide 10: NPDES Background
Regional Boards
North Coast
San Francisco Bay
Central Coast
Los Angeles
Central Valley
Lahontan
Colorado River
Santa Ana
San Diego

## Slide 11: NPDES Background
State Water Quality Control Board
Develop Statewide permits (e.g. Construction Permit, Trash Policy)
Make decisions on policies that apply statewide
Provides guidance to Regional Boards
Regional Water Quality Control Board
Assign Beneficial uses to water bodies in their watershed
  REC1 – contact with water (swimming, etc.)
  REC2 – Non contact with water (hiking, etc.)
Water Quality standards that support Beneficial Uses
Ensure compliance with Permits
  Municipalities with MS4 permits
  State permitted activities (Construction, Industrial, etc.)
Project Water Quality Certification (401 certification)

## Slide 12: NPDES Background

## Slide 13: NPDES Background
(Potential) 303(d) Impairments
Verified thru TMDL (Total Daily Max Load) process
TMDLs (& Waste Load Allocations) are then written into MS4 Permits

## Slide 14: NPDES Background
3 Regional Boards in Riverside County
Permits update on roughly a 5 year cycle
To Arizona

## Slide 15: WQMP EVOLUTION
Prior to 2002 Permit
Drain to Pervious
No clear metrics
Projects submitted after January 1, 2005
BMPs of High or Medium Effectiveness for Pollutants of Concern
Projects entitled after December 6, 2012
LID BMPs only
BioRetention
Santa Ana
San Diego
Whitewater

## Slide 16: APPLICABLE WQMPs
Santa Ana
San Diego
Whitewater
Upcoming
Check with your Co-Permittee. They may have stricter Grandfathering Rules.
Superseded 7/8/18
2005-2012
12/6/2012+
1/1/2015

## Slide 17: Preliminary WQMPs

## Slide 18: Preliminary WQMPs
Why is a Preliminary WQMP required?
The Permit requires:
Preliminary WQMPs for Entitlement
Final WQMP in substantial conformance with the P-WQMP.
Functionality of post-construction BMPs
Track and ensure long term O&M of those BMPs

## Slide 19: Preliminary WQMPs
The Purpose of a P-WQMP is to determine FEASIBILITY and secure the SCOPE of the WQMP.
The 3 key factors:
WQMP Applicability
BMP Type (Required Hierarchy)
BMP sizing

## Slide 20: Preliminary WQMPs
Applicability

## Slide 21
WQMP Applicability | Santa Ana | San Diego | Whitewater
New Development | 10,000 FT2 of Imperviousness |  | Home subdiv. w/ 10 housing units. OR Comm/Industrial projects 100,000 FT2
Redevelopment | 5,000 FT2 of Imperviousness |  | 
Auto Repair | Yes |  | 
Restaurants | 5,000FT2 |  | 
Hillside Dev. | 5,000 FT2 of disturbance on any 25%+ natural slope | 5,000 FT2 of impervious for development on 25%+ natural slope. | SFR 10k imperv. w/ natural slopes 25% (or 10% w/ erosive soil.)
Adj. to ESA | 2,500 FT2 of imperviousness w/in 200’ | 2,500 FT2 of imperviousness OR adding imperviousness 10% of predevelopment w/in 200’ | NOT SPECIFICALLY REQUIRED
Parking Lots | 5,000 FT2 exposed to stormwater |  | 5,000 FT2 exposed to stormwater OR 25 spaces
Streets, Hwys, Fwys | 5000 FT2 or Capital Project TPG | 5,000 FT2 | NOT REQUIRED
Gas Stations | 5,000 FT2 of Imperviousness w/ ADT 100 veh. per day |  | 5,000 FT2 in disturbance
Other Posing Threat | Significant Threat | >1 acre & more pollutants | Significant Threat
Preliminary WQMPs

## Slide 22: Preliminary WQMPs
Hierarchy (BMP TYPE)

## Slide 23: Preliminary WQMPs
Santa Ana & San Diego Required BMP Hiearchy:
1.) Infiltration
2.) Harvest & Reuse
3.) BioRetention
4.) BioTreatment
INFILTRATION RATES < 1.6 in/hr
INFILTRATION RATES < 0.3 in/hr
Infiltration testing is required prior to entitlements
, unless
Small Projects w/ “D” Type Soils (low infil. rates) do not need infiltration testing |  | 
Residential | Commercial | Industrial
< 10ac.& 30 D.U. | < 5ac.& 50k sq.ft. Imperv. | < 2 ac.& 20k sq.ft. Imperv.

## Slide 24: Preliminary WQMPs
Infiltration Testing
BMPs size increases up to 333% if test are not taken in the location of the BMP.

## Slide 25: DMA TYPes for Santa Ana & San Diego

## Slide 26: Preliminary WQMPs
Infiltration Basins
5’ of permeable soil underneath
Pretreatment required

## Slide 27: Preliminary WQMPs
Harvest and Reuse
Pretreatment is required

## Slide 28: Preliminary WQMPs
BioRetention
Subdrain System

## Slide 29: Preliminary WQMPs
BioTreatment
E.g. EDB’s
  Compacted Floor
  Treats thru settling

## Slide 30: Preliminary WQMPs
Whitewater (BMP Type Selection)
(To the extent feasible) LID/Site Design BMPs used to satisfy the Treatment Control BMP requirement must:
Promote retention and/or feature a natural treatment mechanism. Examples include, but are not limited to: extended detention basins, retention basins, drywells, and naturally-lined swales and filter strips; and
Have medium or high effectiveness in reducing those Pollutants of Concern causing Receiving Water impairment.

## Slide 31: Preliminary WQMPs
BMP Sizing

## Slide 32: Preliminary WQMPs
Sizing BMPs
Quality | Quantity | 
VBMP – Volume for the BMP | HydroModification or HCOC’s (hydrologic conditions of concerns) | In addition the project must comply with Drainage Law (i.e. mitigate increased runoff)
Based on 85th percentile storm | Santa Ana: 2yr – 24hr | 
 | San Diego: Flowrate & Durations less than pre-dev. From 10% of 2yr to 10yr for entire rainfall record (continuous simulation) | 
 | Whitewater: Detention or Retention for the 100yr. for drainage law compliance. | 

## Slide 33
What areas need to be treated with a WQMP?
You don’t need to treat areas that drain around the proposed BMPs.
Preliminary WQMPs

## Slide 34
  So what do these sizing calculations look like?
Preliminary WQMPs

## Slide 35
  Water Quality
BMP Sizing
Calculate VBMP
then size BMP

## Slide 36
  Water Quantity – HCOC/Hydromodification
  Santa Ana Region WhiteWater Region Santa Margarita Region
BMP Sizing
SMRHM by Clear Creek Solutions
CivilD with Basin Routing
CivilD or Hydrology Manual Shortcut for Retention
County HydroMod Iterative Spreadsheet Model

## Slide 37
  BMP Size is OFTEN Governed by
  HCOC/HydroMod
BMP Sizing
Water Quality
HCOC
Water Quality
HCOC
Size of BMP

## Slide 38: Preliminary WQMPs
The 3 key factors for P-WQMP’s are:
WQMP Applicability
BMP Type (Required Hierarchy)
BMP sizing
FEASIBILITY
RECAP
Conservative Analysis can be used to show Feasibility

## Slide 39: Final WQMPs

## Slide 40: Final WQMPs
Complete the Template
                F-WQMP is substantially conforming with P-WQMP
                Consistent with Improvement Plans

## Slide 41: MS4 Permit Negotiations

## Slide 42: Released Draft
https://www.waterboards.ca.gov/santaana/water_issues/programs/stormwater/

## Slide 43: Released Draft

## Slide 44: Released Draft
Some Institutional Barriers may include:
State Subdivision Map act 66462.5 may require waiving off-site improvements, including the BMPs are if they are “offsite”.
There are concerns with CEQA clearance. Private Development would need to expand their CEQA footprint to cover offsite improvements.
Maintenance Entities (CFD’s, CSA’s, LMD’s) would not be fully funded until all contributing projects are completed. BMPs without proper maintenance will fail.
However, a credit system may work on a project by project basis.

## Slide 45: Released Draft
It could be interpreted that existing WQMPs would need to be upgraded to the latest WQMP requirements, which may not be feasible if there are R/W constraints. This could require digging out the BMP for infiltration testing and changing the size and shape of the BMP.
that pertain to the WQMP requirements at the time the WQMP was approved.

## Slide 46: Released Draft
The original language triggered projects that may not have been intended to require WQMP. For example, if a Single family home project had steep slopes on the property, but was only developing on the existing flat areas this would trigger WQMP with the existing language.
Disturbing more than 5,000 square feet of slope where the natural slope is 25% or more, or slope areas with known erosive soil conditions.

## Slide 47: Released Draft
The roads are typically lower than the proposed development, which would make many situations technically infeasible to drain the road runoff to the on-site BMPs. It would be within the maximum extent practicable to be able to handle the streets as part of private development with Green Streets treatment.

## Slide 48: Released Draft
Additional right-of-way in of itself does not contribute toward increased potential for pollutant generation.
Replacement is generally for replacing failing asphalt for the benefit of the traveling public, or to address safety issues with design speeds. Replacement is not done without a reasonable purpose.
Why not allow Green Streets for projects that cannot physically drain on-site for treatment?

## Slide 49: Released Draft
Volume and time of concentration cannot be technically mitigated for unless the site can fully infiltrate the difference between the pre- and post-development flows. This is not technically feasible.
Imagine your BMP that is 10% of your site, is required to infiltrate the difference between the pre- and post- development volume.

## Slide 50: Released Draft
2010 Permit Language:

## Slide 51: Questions
https://rcwatershed.org/watersheds/whitewater-river-watershed/
https://trans.rctlma.org/wqmp-water-quality-management-plans
https://trans.rctlma.org/forms-applications
https://building.rctlma.org/forms
https://rcwatershed.org/watersheds/santa-margarita-river-watershed/smrwma-clearinghouse
Santa Margarita WQMP:
https://rcwatershed.org/watersheds/middle-santa-ana-river-watershed/
Santa Ana WQMP:
Whitewater WQMP:
County WQMP website:
BMP Agreement and other useful forms & applications:
Grading and WQMP Cert Forms:
Would you like to see the Hydromod Spreadsheet?